V4L2 Framework
By,
RB Jagadeesh

---
Contents
- V4l2 introduction
- Terminology
- Registration of v4l2 with UVC driver
- Application interacting with v4l2

---
V4L2
- video for Linux 2 is a set of APIs and standards for handling video devices on Linux.
- all the v4l2 devices would be char type device and each devices get represented by its names in the /dev tree like /dev/video.
- v4l2 API includes a very long list of driver callbacks to respond to many ioctl() commands made available to user space.

---
V4L2
App
User space
Kernel Space
V4L2-Core
Camera Driver
(UVC Driver)
Hardware
Camera

---
Terminology
- Resolution
- Aspect Ratio
- color conversion
- Frame rate

---
Terminology
- Resolution: Resolution is number of pixels arranged horizontally and vertically on a monitor.
- Most common resolutions : 720P (HD), 1080P (Full HD), 1440P (QHD), 4K – 2160P (Ultra HD), 8K – 4320P (Ultra HD)
- 720p and 720i
- P stands for progressive
- I stands for interlaced

---
Terminology
- Aspect Ratio : Aspect ratio is relation between width and height
- Depending on the aspect ratio of your display, you are able to use only resolutions that are specific to its width and height.
- 4:3 aspect ratio resolutions: 640×480, 960×720, 1024×768, 1440×1080 and 2048×1536.
- 16:10 aspect ratio resolutions: 1280×800, 1440×900.
- 16:9 aspect ratio resolutions:1280×720, 1920×1080, 2560×1440 and 3840×2160.

---
Terminology
- RGB : RGB color space or RGB color system constructs all the colors from the combination of the Red, Green and Blue colors.
- The red, green and blue use 8 bits each, which have integer values from 0 to 255. This makes 256*256*256=16777216 possible colors.
- YUV : YUV is a way of breaking the brightness and colors in the image down into numbers.
- Y → Luminance and UV → Chrominance

---
Terminology
- Most cameras take the light coming into the lens, and convert that into 3 sets of numbers, one for Red, one for Green, and one for Blue(RGB).
- If we need to lower the brightness uniformly on an image, we need to do it to all 3 colors. There’s also a LOT of redundancy in the data.
- To solve this there we need to convert from RGB to YUV.
- Which breaks the signal down into a Y, or luminance channel, and 2 channels that store color info without brightness info – a Blue channel and a Red channel that don’t contain any brightness.

---
Terminology
Frame rate :
- Frame rate is known as frames per second and fps.
- The rate at which consecutive images called frames are displayed on display.
- Common fps : 24fps, 30fps and 60fps.

---
Registration of v4l2 with UVC driver
uvc_probe()
V4L2_device_register()
uvc_register_video()
uvc_queue_init()
uvc_video_init()
uvc_fops
video_register_device

---
Registration of v4l2 with UVC driver
- v4l2_device_register(struct device *, struct v4l2_device *)
- Registering the v4l2 device instance.
- Initializing buffer queue using uvc_queue_init(struct uvc_video_queue *, enum v4l2_buf_type)
- Initialize struct v4l2_fops file operations with uvc_fops.
- Register the video device and creating the character device file(/dev/video0)

---
V4L2 driver structures
static const struct v4l2_ioctl_ops camera_ioctl_ops = {
        /* overlay */
        .vidioc_enum_fmt_vid_overlay = vidioc_enum_fmt_vid_overlay,
        .vidioc_g_fmt_vid_overlay = vidioc_g_fmt_vid_overlay,
        .vidioc_try_fmt_vid_overlay = vidioc_try_fmt_vid_overlay,
        .vidioc_s_fmt_vid_overlay = vidioc_s_fmt_vid_overlay,
        .vidioc_overlay = vidioc_overlay,
        .vidioc_g_fbuf = vidioc_g_fbuf,
        .vidioc_querycap = vidioc_querycap,
        .vidioc_enum_fmt_vid_cap = vidioc_enum_fmt_vid_cap,
        .vidioc_g_fmt_vid_cap = vidioc_g_fmt_vid_cap,
        .vidioc_try_fmt_vid_cap = vidioc_try_fmt_vid_cap,
        .vidioc_s_fmt_vid_cap = vidioc_s_fmt_vid_cap,

---
V4L2 driver structures
        /* buffer management */
        .vidioc_reqbufs = uvc_ioctl_reqbufs,
        .vidioc_create_bufs = uvc_ioctl_create_bufs,
        .vidioc_querybuf = uvc_ioctl_querybuf,
        .vidioc_qbuf = uvc_ioctl_qbuf,
        .vidioc_dqbuf = uvc_ioctl_dqbuf,
        .vidioc_enum_framesizes = vidioc_enum_framesizes,
        .vidioc_enum_frameintervals = vidioc_enum_frameintervals,
        .vidioc_g_parm = vidioc_g_parm,
        .vidioc_s_parm = vidioc_s_parm,
        .vidioc_streamon = uvc_ioctl_streamon,
        .vidioc_streamoff = uvc_ioctl_streamoff,
}
Struct v4l2_ioctl_info *ioctl_info;

---
V4L2 driver structures
static const struct v4l2_file_operations camera_fops = {
        .owner = THIS_MODULE,
        .open = v4l2_fh_open,
        .release = uvc_fop_release,
        .read = uvc_fop_read,
        .poll = uvc_fop_poll,
        .unlocked_ioctl = video_ioctl2, /* V4L2 ioctl handler */
        .mmap = uvc_fop_mmap,
};

---
File operations
static const struct file_operations v4l2_fops = {
        .owner = THIS_MODULE,
        .read = v4l2_read,
        .write = v4l2_write,
        .open = v4l2_open,
        .get_unmapped_area = v4l2_get_unmapped_area,
        .mmap = v4l2_mmap,
        .unlocked_ioctl = v4l2_ioctl,
        .release = v4l2_release,
        .poll = v4l2_poll,
        .llseek = no_llseek,
}

---
Application interacting with v4l2
VIDIOC_S_FMT--> Set format
VIDIOC_G_FMT-->Get format
VIDIOC_QBUF-->To place video buffer to the buffer queue.
VIDIOC_DQBUF-->To dequeue a video buffer from the buffer queue.
VIDIOC_STREAMON-->To start video capture functionality
VIDIOC_STREAMOFF-->To stop video capture functionality

---
Application interacting with v4l2
Application
/dev/video0
VIDIOC_QUERYCAP
VIDIOC_REQBUF
VIDIOC_QBUF
VIDIOC_STREAMOFF
VIDIOC_DQBUF
VIDIOC_STREAMON

---
Commands to run v4l2 utility
- v4l2-ctl –list-devices
- v4l2-ctl –list-formats
- v4l2-ctl –set-fmt-video=width=1920,height=1080,pixelformat=1
- v4l2-ctl --stream-mmap=3 --stream-count=100 –stream-to=somefile.mp4
- v4l2-ctl -d /dev/video -P
- v4l2-ctl -p 30